## Slide 1: Advanced Computer Architecture (ACA 2019)
Dr. ZHANG Chun-yuan
College of Computer, NUDT
Fall, 2019

## Slide 2: Lecture 06 Tomasulo's Algorithm
November 13, 2019

## Slide 3: The Front Panel of System 360 Model 91 -- from Internet

## Slide 4: Buffer
Functions
Queue
Virtual function units

## Slide 5: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6

## Slide 6: Fields of Reservation Stations
Op: The operation to perform
Vj, Vk: value of the source operands
Qj, Qk: RSs producing source registers
  Qj, Qk = 0 => ready
  Only one of V or Q is valid for each operand
Busy: indicates this reservation station and its accompanying FUs are occupied

## Slide 7: Register File Has a Field
Qi: the reservation station that contains the operation whose result should be stored into this register
  If the value of Qi is blank (0), no currently active instruction is computing a result for this register (where is the value?)

## Slide 8: Load And Store Buffers
Each have a filed A
  A: hold the effective address
The store buffer also has a V field
  V: value of the operands

## Slide 9: How It Works: Previous Example
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 10: Latencies and Checking Points
Latencies
  Load is 1 clock cycle
  Add/sub is 2
  Multiply is 10
  Divide is 40

## Slide 11: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 12: Tomasulo Example Cycle 1

## Slide 13: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding?

## Slide 14: Tomasulo Example Cycle 3
Note: MULT issued, registers are removed (“renamed”) in RSs
Load1 exec completing; what is waiting for Load1?

## Slide 15: Tomasulo Example Cycle 4
Load2 exec completing

## Slide 16: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1
May F0 course a error?

## Slide 17: Tomasulo Example Cycle 6
Issue ADDD here despite name dependency on F6?

## Slide 18: Tomasulo Example Cycle 7
Add1 (SUBD) completing; what is waiting for it?

## Slide 19: Tomasulo Example Cycle 8

## Slide 20: Tomasulo Example Cycle 9

## Slide 21: Tomasulo Example Cycle 10
Add2 (ADDD) completing; what is waiting for it?

## Slide 22: Tomasulo Example Cycle 11
Write result of ADDD here?
All quick instructions complete in this cycle!

## Slide 23: Tomasulo Example Cycle 12

## Slide 24: Tomasulo Example Cycle 13

## Slide 25: Tomasulo Example Cycle 14

## Slide 26: Tomasulo Example Cycle 15
Mult1 (MULTD) completing.Who is waiting?

## Slide 27: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 28: Tomasulo Example Cycle 16-54
Faster than light computation (skip a couple of cycles)

## Slide 29: Tomasulo Example Cycle 55

## Slide 30: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing. Who is waiting?

## Slide 31: Tomasulo Example Cycle 57
In-order issue, o-o-o exec and o-o-o completion.

## Slide 32: Steps in the Algorithm and What Is Required for Each Step p180, 5ed/p205, 6ed
Self learning

## Slide 33: The Code
Loop: fld f0,0(x1)
fmul.d f4,f0,f2
fsd f4,0(x1)
addi x1,x1,-8
bne x1,x2,Loop
// branches if x16 != x2

## Slide 34: Snapshot Time Assume
All branches are taken!
All of the instructions in two successive iterations of the loop have issued
  But none has completed
The load and store buffers contain the addresses to be loaded from and stored to
  The load values are in the load buffers
  The store buffers indicate that the multiply destinations are the values to store

## Slide 35: Two Active Iterations of The Loop with no Instruction Yet Completed
Self learning

## Slide 36: Next …
Hardware-Based Speculation

## Slide 37: HW Speculation and Prediction
HW speculation is subtle, but important, extension over branch prediction with dynamic scheduling
HW speculation
  Fetch, issue, and execute instructions, as if predictions are always correct
  Dynamic scheduling only fetches and issues such instructions

## Slide 38: What about Precise Exceptions/Interrupts?
Recall: an exception is precise if there is a single instruction for which:
  All instructions before that have committed (finished) their state
  No following instructions (including the interrupting instruction) have modified any state
Both Scoreboard and Tomasulo have
  In-order issue
  out-of-order execution
  out-of-order completion --> we need order

## Slide 39: Done execute
Deposit result in ROB slot
Mark exception state
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 40: On issue
Reserve slot at tail of ROB
Record dest reg, PC
Tag u-op with ROB slot
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 41: WB head of ROB
Check exception, handle
Write register value, or
Commit the store
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 42: Reorder Buffer + Forwarding
Forwarding committing results to later uncommitted operations
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 43: Reorder Buffer + Forwarding + Speculation
Issue branch into ROB
Mark with prediction
Fetch and issue predicted instructions speculatively
Branch must resolve before leaving ROB
Resolve correct
  Commit following instr
Resolve incorrect
  Mark following instr in ROB as invalid
  Let them clear
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 44: What is that like?
Tomasulo's!
The key ideas
  Out-of-order execution
  Force them to in order commit
    Prevent any irrevocable action, such as an exception, until an instruction commits
Instruction Fetch
Issue
Write Back
Register File
FU
ROB

## Slide 45: 3 components of HW-based speculation
Dynamic branch PREDICTION to choose which instructions to execute
Dynamic SCHEDULING different combinations of basic blocks
Speculation allow EXECUTION of instructions before control dependences are resolved
  Ability to UNDO incorrectly speculated

## Slide 46: Reorder Buffer (ROB)
Reorder
Buffer
FP
Op
Queue
FP Adder
FP Adder
Res Stations
Res Stations
FP Regs
Commit path

## Slide 47: Fields of ROB 1/2
1. Instruction type (op code): indicates instructions
  A branch (and has no destination result)
  A store (which has a memory address destination)
  A register operation (ALU operation or load, which have register destinations)

## Slide 48: Fields of ROB 2/2
2. Destination field: where the instruction result should be written
  The register number (for loads and ALU operations)
  The memory address (for stores)
3. Value: hold the value of the instruction result until the instruction commits
4. Ready: indicates that instruction has completed execution, and the value is ready

## Slide 49: RV with ROB Using Tomasulo's
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 50: Speculation: Original
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 51: Speculation: Clock 1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fld f6,32(x2)
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 32+x2
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 52: Speculation: Clock 2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f2
f6
fld f2,44(x3)
fld f6,32(x2)
y
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 32+x2
2 44+x3
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 53: Speculation: Clock 3
Write Result
3 fmul.d ROB2,f4
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f0
f2
f6
M(32+x2)
fmul.d f0,f2,f4
fld f2,44(x3)
fld f6,32(x2)
y
y
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
1 32+x2
2 44+x3
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 54: Speculation: Clock 4-1
3 fmul.d ROB2,f4
4 fsub.d ROB2,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f8
fsub.d f8,f2,f6
y
f0
f2
fmul.d f0,f2,f4
fld f2,44(x3)
y
y
n
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 44+x3
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2
Committed
Write Result

## Slide 55: Speculation: Clock 4-2
3 fmul.d M(44+x3),f4 10
4 fsub.d M(44+x3),f6 2
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f8
fsub.d f8,f2,f6
y
f0
f2
M(44+x3)
fmul.d f0,f2,f4
fld f2,44(x3)
y
y
n
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 44+x3
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2
Write Result
Start to run

## Slide 56: Speculation: Clock 5
3 fmul.d M(44+x3),f4 9
5 fdiv.d ROB3,f6
4 fsub.d M(44+x3),f6 1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f0
fdiv.d f0,f0,f6
y
f8
fsub.d f8,f2,f6
y
f0
f2
M(44+x3)
fmul.d f0,f2,f4
fld f2,44(x3)
y
n
Busy?
Dest
Dest
Oldest
Newest
from
Memory
2 44+x3
Dest
Reorder Buffer
Registers
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2
Committed

## Slide 57: Speculation: Clock 6
3 fmul.d M(44+x3),f4 8
5 fdiv.d ROB3,f6
4 fsub.d M(44+x3),f6 0
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d ROB4,f2
1. fld f6,32(x2)
2. fld f2,44(x3)
3. fmul.d f0,f2,f4
4. fsub.d f8,f2,f6
5. fdiv.d f0,f0,f6
6. fadd.d f6,f8,f2

## Slide 58: Speculation: Clock 7-1
3 fmul.d M(44+x3),f4 7
5 fdiv.d ROB3,f6
4 fsub.d M(44+x3),f6 -
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d ROB4,f2
Write Result

## Slide 59: Speculation: Clock 7-2
3 fmul.d M(44+x3),f4 7
5 fdiv.d ROB3,f6
4 fsub.d M(44+x3),f6 -
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d f2-f6,f2 2
Write Result

## Slide 60: Speculation: Clock 8
3 fmul.d M(44+x3),f4 6
5 fdiv.d ROB3,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d f2-f6,f2 1

## Slide 61: Speculation: Clock 9
3 fmul.d M(44+x3),f4 5
5 fdiv.d ROB3,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d f2-f6,f2 0

## Slide 62: Speculation: Clock 10-1
Write Result
3 fmul.d M(44+x3),f4 4
5 fdiv.d ROB3,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
6 fadd.d f2-f6,f2 0

## Slide 63: Speculation: Clock 10-2
3 fmul.d M(44+x3),f4 4
5 fdiv.d ROB3,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 64: Speculation: Clock 11-14
3 fmul.d M(44+x3),f4 0
5 fdiv.d ROB3,f6
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 65: Speculation: Clock 15
3 fmul.d M(44+x3),f4 -
5 fdiv.d f2*f4,f6 40
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
f2*f4
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Write Result

## Slide 66: Speculation: Clock 16
Committed
5 fdiv.d f2*f4,f6 39
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
f0
f2*f4
fmul.d f0,f2,f4
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 67: Speculation: Clock 17
5 fdiv.d f2*f4,f6 38
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
f8
f2-f6
fsub.d f8,f2,f6
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 68: Speculation: Clock 18
5 fdiv.d f2*f4,f6 37
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 69: Speculation: Clock 55
5 fdiv.d f2*f4,f6 0
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
fdiv.d f0,f0,f6
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 70: Speculation: Clock 56
5 fdiv.d f2*f4,f6 -
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
f0/f6
fdiv.d f0,f0,f6
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 71: Speculation: Clock 57
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
f0
f0/f6
fdiv.d f0,f0,f6
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 72: Speculation: Clock 58
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
f6
f8-f2
fadd.d f6,f8,f2
y
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
Committed

## Slide 73: Speculation: Clock 59
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
Busy?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers

## Slide 74: Stages of Tomasulo's Speculation
Issue
Execute
Write result
Commit
  Additional stage

## Slide 75: Homework
Textbook:
  Algorithms and execution evaluation
    3.5, 3.6
  How does a loop run in?
Coding Tomasulo's (w/ & w/o speculation)
Papers
  "An Efficient Algorithm for Exploiting Multiple Arithmetic units", Tomasulo, IBM Journal, January 1967
Homeworks

## Slide 76: Next …
Multiple Issue